Total Cost for parts: 1.48

Items Used:
-socket wrench
-10mm socket
-13mm socket
-1/4" socket adapter 
-flat and phillips head screw driver
-steel wool
-glass cleaner
-paper towels
-black silicone sealant
-razor blade
-1" nylon hole plug
-1 ear plug ... (you'll see)
-electrical tape

Heres a before shot with the wiper arm still on:

Open the hatch and remove the 2 screws where shown:

Use some force and pull it off:

On the outside of the hatch remove the cover on the wiper:

13mm socket and flat head screw driver used here:

Remove the power plug and the washer fluid line:

I used an ear plug (can use something else) to "clog" the fluid line and then taped it so it will hold in place, its good if you ever need to put the wiper back on it should easily come out:

Roll the ear plug up like you would for your ear then insert it into the line:

Now tape it up:

Remove the nuts shown with your 10mm socket:

After removing the wiper motor you are left with the rubber insert in the glass, remove this:

I cleaned the glass up where the rubber insert was with some glass cleaner and some steel wool because the grime wasn't coming off with just paper towels.

Now get out the hole plug and some sort of silicone sealant:

Goo up the glass good:

Plop it on in

Now goo up the inside so you have a nice tight seal:

You can now put everything back together, after letting silicone sealant dry up on the outside, trim off the excess with a razor blade, be careful not to slice up your nylon hole pug so it looks fresh.

I had some residue on my glass from the silicone so I used some glass cleaner and went at it with the steel wool and there you have it:

After shot: